## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 5 Network Layer:
Control Plane
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
Re-do of network management slides; redo of Bellman-Ford slides

## Slide 2: Network layer: “control plane” roadmap
introduction
routing protocols
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 3: Making routing scalable
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice
scale: billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy:
Internet: a network of networks
each network admin may want to control routing in its own network

## Slide 4: Internet approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
intra-AS (aka “intra-domain”): routing among within same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocols
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es
inter-AS (aka “inter-domain”): routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)

## Slide 5: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
intra-AS
routing
intra-AS
routing
intra-AS
routing
inter-AS routing
forwarding
table
forwarding table configured by intra- and inter-AS routing algorithms
Intra-AS
Routing
Inter-AS
Routing
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations

## Slide 6: Inter-AS routing: a role in intradomain forwarding
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
other
networks
other
networks
suppose router in AS1 receives datagram destined outside of AS1:
AS1 inter-domain routing must:
learn which destinations reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
  router should forward packet to gateway router in AS1, but which one?

## Slide 7: Inter-AS routing: routing within an AS
most common intra-AS routing protocols:
RIP: Routing Information Protocol [RFC 1723]
  classic DV: DVs exchanged every 30 secs
  no longer widely used
EIGRP: Enhanced Interior Gateway Routing Protocol
  DV based
  formerly Cisco-proprietary for decades (became open in 2013 [RFC 7868])
OSPF: Open Shortest Path First [RFC 2328]
  link-state routing
  IS-IS protocol (ISO standard, not RFC standard) essentially same as OSPF

## Slide 8: OSPF (Open Shortest Path First) routing
“open”: publicly available
classic link-state
  each router floods OSPF link-state advertisements (directly over IP rather than using TCP/UDP) to all other routers in entire AS
  multiple link costs metrics possible: bandwidth, delay
  each router has full topology, uses Dijkstra’s algorithm to compute forwarding table
security: all OSPF messages authenticated (to prevent malicious intrusion)

## Slide 9: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements flooded only in area, or backbone
  each node has detailed area topology; only knows direction to reach other destinations
area border routers: “summarize” distances to destinations in own area, advertise in backbone
area 1
area 2
area 3
backbone
internal
routers
backbone router: runs OSPF limited to backbone
boundary router: connects to other ASes
local routers:
flood LS in area only
compute routing within area
forward packets to outside via area border router

## Slide 10: Network layer: “control plane” roadmap
introduction
routing protocols
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 11: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
allows subnet to advertise its existence, and the destinations it can reach, to rest of Internet: “I am here, here is who I can reach, and how”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy

## Slide 12: eBGP, iBGP connections
eBGP connectivity
logical iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protocols

## Slide 13: BGP basics
when AS3 gateway 3a advertises path AS3,X to AS2 gateway 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
BGP advertisement:
AS3, X

## Slide 14: Path attributes and BGP routes
BGP advertised route: prefix + attributes
  prefix: destination being advertised
  two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes

## Slide 15: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c
AS3, X

## Slide 16: BGP path advertisement (more)
AS2,AS3,X
AS1 gateway router 1c learns path AS2,AS3,X from 2a
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
based on policy, AS1 gateway router 1c chooses path AS3,X and advertises path within AS1 via iBGP
AS3, X
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS3,X
AS3,X
AS3,X

## Slide 17: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 18: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS2,AS3,X
AS3,X
AS3, X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
1
2
dest
interface
…
…
…
…
local link interfaces
at 1a, 1d
at 1d: to get to X, use interface 1
1c
1
X
1
AS3,X
AS3,X
AS3,X

## Slide 19: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
at 1d: to get to X, use interface 1
dest
interface
…
…
…
…
1c
2
X
2
at 1a: OSPF intra-domain routing: to get to 1c, use interface 2
at 1a: to get to X, use interface 2

## Slide 20: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its network
intra-AS: single admin, so policy less of an issue
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy dominates over performance

## Slide 21: Hot potato routing
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
AS3,X
AS1,AS3,X
OSPF link weights
201
112
263

## Slide 22: BGP: achieving policy via advertisements
B
legend:
customer
network:
provider
network
A advertises path Aw to B and to C
B chooses not to advertise BAw to C!
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,w
A,w

## Slide 23: BGP: achieving policy via advertisements (more)
B
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,B,C are provider networks
x,w,y are customer (of provider networks)
x is dual-homed: attached to two networks
policy to enforce: x does not want to route from B to C via x
  .. so x will not advertise to B a route to C
legend:
customer
network:
provider
network

## Slide 24: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 25: Network layer: “control plane” roadmap
introduction
routing protocols
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 26: Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 27: Software defined networking (SDN)
Why a logically centralized control plane?
easier network management: avoid router misconfigurations, greater flexibility of traffic flows
table-based forwarding (recall OpenFlow API) allows “programming” routers
  centralized “programming” easier: compute tables centrally and distribute
  distributed “programming” more difficult: compute tables as result of distributed algorithm (protocol) implemented in each-and-every router
open (non-proprietary) implementation of control plane
  foster innovation: let 1000 flowers bloom

## Slide 28: Traffic engineering: difficult with traditional routing
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Q: what if network operator wants u-to-z traffic to flow along uvwz, rather than uxyz?
A: need to re-define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
link weights are only control “knobs”: not much control!

## Slide 29: Traffic engineering: difficult with traditional routing
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can’t do it (or need a new routing algorithm)

## Slide 30: Traffic engineering: difficult with traditional routing
Q: what if w wants to route blue and red traffic differently from w to z?
A: can’t do it (with destination-based forwarding, and LS, DV routing)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
We learned in Chapter 4 that generalized forwarding and SDN can be used to achieve any routing desired

## Slide 31: Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized “flow-based” forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane functions external to data-plane switches
…
routing
access control
load
balance
4. programmable control applications

## Slide 32: Software defined networking (SDN)
Data-plane switches:
fast, simple, commodity switches implementing generalized data-plane forwarding (Section 4.4) in hardware
flow (forwarding) table computed, installed under controller supervision
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable, what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 33: Software defined networking (SDN)
SDN controller (network OS):
maintain network state information
interacts with network control applications “above” via northbound API
interacts with network switches “below” via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 34: Software defined networking (SDN)
network-control apps:
“brains” of control: implement control functions using lower-level services, API provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 35: Components of SDN controller
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
communication: communicate between SDN controller and controlled switches
network-wide state management : state of networks links, switches, services: a distributed database
interface layer to network control apps: abstractions API

## Slide 36: OpenFlow protocol
operates between controller, switch
TCP used to exchange messages
  optional encryption
three classes of OpenFlow messages:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (misc.)
OpenFlow Controller

## Slide 37: OpenFlow: controller-to-switch messages
Key controller-to-switch messages
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: controller can send this packet out of specific switch port
OpenFlow Controller

## Slide 38: OpenFlow: switch-to-controller messages
Key switch-to-controller messages
packet-in: transfer packet (and its control) to controller. See packet-out message from controller
flow-removed: flow table entry deleted at switch
port status: inform controller of a change on a port.
Fortunately, network operators don’t “program” switches by creating/sending OpenFlow messages directly. Instead use higher-level abstraction at controller
OpenFlow Controller

## Slide 39: SDN: control/data plane interaction example
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Dijkstra’s link-state
routing
s1
s2
s3
s4
S1, experiencing link failure uses OpenFlow port status message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra’s routing algorithm application has previously registered to be called when ever link status changes. It is called.
3
Dijkstra’s routing algorithm access network graph info, link state info in controller, computes new routes
4
1
2
3
4

## Slide 40: SDN: control/data plane interaction example
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Dijkstra’s link-state
routing
s1
s2
s3
s4
link state routing app interacts with flow-table-computation component in SDN controller, which computes new flow tables needed
5
controller uses OpenFlow to install new tables in switches that need updating
6
5
6
1
2
3
4

## Slide 41: OpenDaylight (ODL) controller
Network Orchestrations and Applications
Southbound API
Service Abstraction Layer (SAL)
config. and operational data store
REST/RESTCONF/NETCONF APIs
messaging
OpenFlow
NETCONF
SNMP
OVSDB
…
Northbound API
Traffic Engineering
…
Firewalling
Load Balancing
Basic Network Functions
Enhanced Services
…
…
Forwarding rules mgr.
AAA
Host
Tracker
Stats
mgr.
Switch
mgr.
Topology
processing
Service Abstraction Layer:
interconnects internal, external applications and services

## Slide 42: ONOS controller
Network Applications
Southbound API
Northbound API
Traffic Engineering
…
Firewalling
Load Balancing
southbound abstractions,
protocols
OpenFlow
Netconf
OVSDB
device
link
host
flow
packet
northbound abstractions,
protocols
REST API
Intent
ONOS
distributed core
statistics
devices
hosts
links
paths
flow rules
topology
control apps separate from controller
intent framework: high-level specification of service: what rather than how
considerable emphasis on distributed core: service reliability, replication performance scaling

## Slide 43: SDN: selected challenges
hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  robustness to failures: leverage strong theory of reliable distributed system for control plane
  dependability, security: “baked in” from day one?
networks, protocols meeting mission-specific requirements
  e.g., real-time, ultra-reliable, ultra-secure
Internet-scaling: beyond a single AS
SDN critical in 5G cellular networks

## Slide 44: Network layer: “control plane” roadmap
introduction
routing protocols
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 45: ICMP: internet control message protocol
used by hosts and routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP messages carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 46: Traceroute and ICMP
when ICMP message arrives at source: record RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes
source sends sets of UDP segments to destination
  1st set has TTL =1, 2nd set has TTL=2, etc.
datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message possibly includes name of router & IP address

## Slide 47: Network layer: Summary
we’ve learned a lot!
approaches to network control plane
  per-router control (traditional)
  logically centralized control (software defined networking)
traditional routing algorithms
  implementation in Internet: OSPF , BGP
SDN controllers
  implementation in practice: ODL, ONOS
Internet Control Message Protocol
next stop: link layer!