## Slide 1: Cache
Compiled by:
Sarosh shahid

## Slide 2: LRU bit
Least recently used (LRU) replacement: the least recently used block in a set evicted in case of N-associative and fully associative caches.
In case of 2-way associative cache, 1-bit is required to keep check of recently used data block.
  When a block is accessed its LRU bit will be set to zero (now it’s the least recently used data) and increment all the other values of LRU bit accordingly.
  When data is to be evicted from a block, replace the block with maximum value of LRU bit (1 in 2-way associative, 2 in 4-way associative and so on).
LRU bit | Data block
01 | D0
00 | D1
11 | D2
10 | D3
Example : Set “i” of a 4-way associative cache
The LRU bit indicates the sequence of memory access only for this particular set was in order –
D2 D3 D0 D1
And D1 with the least LRU bit value is the most recently accessed

## Slide 3: LRU bit
Least recently used (LRU) replacement: the least recently used block in a set evicted in case of N-associative and fully associative caches.
LRU bit | Data block
01 | D0
00 | D1
11 | D2
10 | D3
Example : Set “i” of a 4-way associative cache
LRU bit | Data block
10 | D0
01 | D1
11 | D2
00 | D3
After the data D3 is accessed again
Set the least recently used D3 to 0 and increment all the remaining bit accordingly

## Slide 4: Example 02
Convert to
binary
b = 2B
C = 16B
N = 2 (2-way associative)
Addresses are 8 bits
  B = C/b = 16/2 = 8
S = B/N = 8/2 = 4
Processor Memory Access Sequence
0xFF
0x96
0x1E
0x97
0X07
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | 
FD | FD
FE | FE
FF | FF
Memory
Cache
0xFF
1111 1111
Tag Bits Set bits Offset bits
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 0 |  |  |  | 
 | 0 |  |  |  | 
Cache Miss = 1 Cache Hit = 0
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 0 | 11111 | FE | FF
 | 0 |  |  |  | 

## Slide 5: Example 02
Convert to
binary
b = 2B
C = 16B
N = 2 (2-way associative)
Addresses are 8 bits
  B = C/b = 16/2 = 8
S = B/N = 8/2 = 4
Processor Memory Access Sequence
0xFF
0x96
0x1E
0x97
0X07
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | 
FD | FD
FE | FE
FF | FF
Memory
Cache
0x96
1001 0110
Tag Bits Set bits Offset bits
Cache Miss = 2 Cache Hit = 0
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 0 | 11111 | FE | FF
 | 0 |  |  |  | 
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 1 | 11111 | FE | FF
 | 1 | 0 | 10010 | 96 | 97

## Slide 6: Example 02
Convert to
binary
b = 2B
C = 16B
N = 2 (2-way associative)
Addresses are 8 bits
  B = C/b = 16/2 = 8
S = B/N = 8/2 = 4
Processor Memory Access Sequence
0xFF
0x96
0x1E
0x97
0X07
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | 
FD | FD
FE | FE
FF | FF
Memory
Cache
0x1E
0001 1110
Tag Bits Set bits Offset bits
Cache Miss = 3 Cache Hit = 0
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 1 | 11111 | FE | FF
 | 1 | 0 | 10010 | 96 | 97
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 0 | 00011 | 1E | 1F
 | 1 | 1 | 10010 | 96 | 97

## Slide 7: Example 02
Convert to
binary
b = 2B
C = 16B
N = 2 (2-way associative)
Addresses are 8 bits
  B = C/b = 16/2 = 8
S = B/N = 8/2 = 4
Processor Memory Access Sequence
0xFF
0x96
0x1E
0x97
0X07
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | 
FD | FD
FE | FE
FF | FF
Memory
Cache
0x97
1001 0111
Tag Bits Set bits Offset bits
Cache Miss = 3 Cache Hit = 1
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 0 | 00011 | 1E | 1F
 | 1 | 1 | 10010 | 96 | 97
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 1 | 00011 | 1E | 1F
 | 1 | 0 | 10010 | 96 | 97

## Slide 8: Example 02
Convert to
binary
b = 2B
C = 16B
N = 2 (2-way associative)
Addresses are 8 bits
  B = C/b = 16/2 = 8
S = B/N = 8/2 = 4
Processor Memory Access Sequence
0xFF
0x96
0x1E
0x97
0X07
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | 
FD | FD
FE | FE
FF | FF
Memory
Cache
0x07
0000 0111
Tag Bits Set bits Offset bits
Cache Miss = 4 Cache Hit = 1
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 1 | 00011 | 1E | 1F
 | 1 | 0 | 10010 | 96 | 97
Sets | V bit | LRU bit | Tags | 0 | 1
00 | 0 |  |  |  | 
 | 0 |  |  |  | 
01 | 0 |  |  |  | 
 | 0 |  |  |  | 
10 | 0 |  |  |  | 
 | 0 |  |  |  | 
11 | 1 | 0 | 00000 | 06 | 07
 | 1 | 1 | 10010 | 96 | 97

## Slide 9: Example 03
Convert to
binary
b = 1B
Full Associative Cache
Single set with 4-ways
Address is 8bits
  C = 1B * 4 (ways) = 4B
  B = C/b = 4/1 = 4
S = B/N = 4/4 = 1
Processor Memory Access Sequence
0x06
Memory
Cache
0x06
0000 0110
Tag Bits Set bits Offset bits
Cache Miss = 1 Cache Hit = 0
Set | V bit | LRU bit | Tags | Data
 | 1 | 00 | 0000 0110 | 06
 | 0 |  |  | 
 | 0 |  |  | 
 | 0 |  |  | 
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | …….
FD | FD
FE | FE
FF | FF

## Slide 10: Example 03
Convert to
binary
b = 1B
Full Associative Cache
Single set with 4-ways
Address is 8bits
  C = 1B * 4 (ways) = 4B
  B = C/b = 4/1 = 4
S = B/N = 4/4 = 1
Processor Memory Access Sequence
0x06
0xEF
Memory
Cache
0xEF
1110 1111
Tag Bits Set bits Offset bits
Cache Miss = 2 Cache Hit = 0
Set | V bit | LRU bit | Tags | Data
 | 1 | 01 | 0000 0110 | 06
 | 1 | 00 | 1110 1111 | EF
 | 0 |  |  | 
 | 0 |  |  | 
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | …….
FD | FD
FE | FE
FF | FF

## Slide 11: Example 03
Convert to
binary
b = 1B
Full Associative Cache
Single set with 4-ways
Address is 8bits
  C = 1B * 4 (ways) = 4B
  B = C/b = 4/1 = 4
S = B/N = 4/4 = 1
Processor Memory Access Sequence
0x06
0xEF
0xB2
Memory
Cache
0xB2
1011 0010
Tag Bits Set bits Offset bits
Cache Miss = 3 Cache Hit = 0
Set | V bit | LRU bit | Tags | Data
 | 1 | 10 | 0000 0110 | 06
 | 1 | 01 | 1110 1111 | EF
 | 1 | 00 | 1011 0010 | B2
 | 0 |  |  | 
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | …….
FD | FD
FE | FE
FF | FF

## Slide 12: Example 03
Convert to
binary
b = 1B
Full Associative Cache
Single set with 4-ways
Address is 8bits
  C = 1B * 4 (ways) = 4B
  B = C/b = 4/1 = 4
S = B/N = 4/4 = 1
Processor Memory Access Sequence
0x06
0xEF
0xB2
0x06
Memory
Cache
0x06
0000 0110
Tag Bits Set bits Offset bits
Cache Miss = 3 Cache Hit = 1
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | …….
FD | FD
FE | FE
FF | FF
Set | V bit | LRU bit | Tags | Data
 | 1 | 00 | 0000 0110 | 06
 | 1 | 10 | 1110 1111 | EF
 | 1 | 01 | 1011 0010 | B2
 | 0 |  |  | 
Respective tag found so it’s a cache hit

## Slide 13: Example 03
Convert to
binary
b = 1B
Full Associative Cache
Single set with 4-ways
Address is 8bits
  C = 1B * 4 (ways) = 4B
  B = C/b = 4/1 = 4
S = B/N = 4/4 = 1
Processor Memory Access Sequence
0x06
0xEF
0xB2
0x06
0x59
Memory
Cache
0x59
0101 1001
Tag Bits Set bits Offset bits
Cache Miss = 4 Cache Hit = 1
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | …….
FD | FD
FE | FE
FF | FF
Set | V bit | LRU bit | Tags | Data
 | 1 | 01 | 0000 0110 | 06
 | 1 | 11 | 1110 1111 | EF
 | 1 | 10 | 1011 0010 | B2
 | 1 | 00 | 0101 1001 | 59

## Slide 14: Example 03
Convert to
binary
b = 1B
Full Associative Cache
Single set with 4-ways
Address is 8bits
  C = 1B * 4 (ways) = 4B
  B = C/b = 4/1 = 4
S = B/N = 4/4 = 1
Processor Memory Access Sequence
0x06
0xEF
0xB2
0x06
0x59
0x23
Memory
Cache
0x23
0010 0011
Tag Bits Set bits Offset bits
Cache Miss = 4 Cache Hit = 1
00 | 00
01 | 01
02 | 02
03 | 03
04 | 04
05 | 05
06 | 06
07 | 07
08 | 08
……. | …….
FD | FD
FE | FE
FF | FF
Set | V bit | LRU bit | Tags | Data
 | 1 | 10 | 0000 0110 | 06
 | 1 | 00 | 0010 0011 | 23
 | 1 | 11 | 1011 0010 | B2
 | 1 | 01 | 0101 1001 | 59

## Slide 15: Types of Cache Misses
Compulsory Miss:
The first request to a cache block is called a compulsory miss, because the block must be read from memory regardless of the cache design.
Capacity Miss:
Capacity misses occur when the cache is too small to hold all concurrently used data.
Conflict Miss:
Conflict misses are caused when several addresses map to the same set and evict blocks that are still needed.

## Slide 16: Cache Parameters
  Increasing cache capacity can reduce conflict and capacity misses, but it does not affect compulsory misses.
  Increasing block size could reduce compulsory misses (due to spatial locality). But as block size increases, the number of sets in a fixed-size cache decreases, increasing the probability of conflicts.
  An N-way set associative cache reduces conflicts by providing N blocks in each set where data mapping to that set might be found. Each memory address still maps to a specific set, but it can map to any one of the N blocks in the set. However, set associative caches are usually slower and somewhat more expensive to build